## Slide 1: Energy Measurement on board Train Systems. Experiences from Bane NOR.
ERESS FORUM June 13th 2019.
Reidun Jørgensen and Dag S. Storhaug, Bane NOR Energi

## Slide 2: EMS Highlights
2019:
In Norway, almost 100% of the vehicles have Energy Measurement Systems onboard.
The number of devices is around 520 units.
Norwegian T.O. are currently working on the second generation of meters to be installed and Commissioned.
The replacement goes fast for some companies and slower for other companies.
Currently 30% of the devices are in compliance with EN50463-2012 norm
The remaining 70% of the devices are going to be replaced. This Devices are installed in the period from 2005-2013.

## Slide 3: Changing to another meter supplier/product for old trains – some experiences
Planning:
For the IM, it’s important in an early stage to collect feedback from the Train Owners according to their experience from previous installations of devices.
Make it possible to use existing cables for sensors for Current transducer, Voltage transformers and power supply for the new devices if the accuracy meet the requirements.
Be aware of interfacing challenges for new devices;
  like, does the physical size of the new device be in accordance with the space available in the cabin in the vehicle?
  Does the existing power supply solution for the EMS meet the needs for another system?
  Are the new device easy install and to do the commissioning of, seen from the installation responsible point on view?

## Slide 4: Changing to another meter supplier/product for old trains – some experiences
Data transfer from the devices to ground by GSM network:
Using of the existing antennas/connectors if possible, for the new devices.
For data transfer to ground, be aware of possible/planned changes for broadband frequencies for the GSM network from the National authorities and the Sim Card provider (GSM Network Operator).
Change of for broadband frequencies can influence on choose of modem for the energy meter, antennas and antenna cables.
In Norway the 3G GSM network broadband frequencies are to be faced out during this year, but 2G GSM network will remain for some more years.